Basic class for non CNC users

Prerequisite:  Basic machining experience

Teaching to be done in a classroom with either a chalk board or white board.  Machine to be used for class must be under power and in working condition.

Students must have:	Safety Glasses

At least 1 copy of the programming manual

Caliper or Micrometer

Paper and writing tool

Materials supplied by instructor:	Cutting tools, blank material, and collet for worked examples in class

Day 1

8:00 to 9:30       	Basic OmniTurn programming and program format. Nomenclature and rules.

Break

9:45: to 11:00     	Write a program – Basic 1 tool program

G90, G72, G94, G95 M30, M08, M03/M05, T1, G10

11:00 to 12:00   	Machine Safety is first!  Review lathe safety and proper usage

Entering the program in the OmniTurn and basic machine functions

Lunch

12:45 to 2:00     	How to run a program for the first time (safely), setting a turning tool

and adjusting offsets

Break

2:15 to 3:30       	Modify the first part to add a second tool, corner chamfer and corner radius

Modify the program to add a threading cycle and peck drill

G33, G83

3:30 to 4:45	Enter the last program, set a c drill, drill, and threading tool.  Run program

4:45 to 5:00	Give class a homework assignment of a simple program for next day

Day 2

8:00 to 8:30       	Go over homework, add new programming features if needed.

8:30 to 9:30     	Enter the program, touch off tools, and correct offsets, run program

Break

9:50 to 12:00	Additional programming examples.

Boring vs turning

Roughing cycles G74, 75, 78

Threading cycles Metric, Multistart, Tapered, Cleanup pass

Write an additional program, either given by teacher or an example from end

user’s requirements, then prep to run parts

Lunch

1:00 to 2:00   	Setup and run an end user’s part, or run given program.

Break

2:15 to 4:00     	Additional programming codes:

Tool nose radius (TNR), Secondary offsets, C axis programming. ETC

4:00 to 5:00       	Question and answers, possibly more homework.

Possible Day 3

Work with end user’s parts, tooling and programs

Additional worked examples supplied by instructor

Service, Maintenance, and trouble shooting.